## Slide 1
Open hardware, open software
https://github.com/open-spectro
mini USB
ATMEGA 32U4
16MHz clock
256 pixels photodiode array
2 white LEDs
1 RGB LED
HOW ?
open-spectrophotometer
Florian, Océane and Luc Patiny, Michaël Zasso
The light produced by white LEDs goes through a sample, is selected by 2 slits and diffracted by a grating film. The diffracted light is analysed by a photodiode array that is connected to the computer.
Compact PCB are designed to use the same micro controller as the Arduino™ Leonardo and is fully compatible with the Arduino™ IDE. This makes it very easy to program.
Communication with the spectrophotometer is done using USB virtual serial port allowing simple control from any program.
A chrome application allows to control directly the spectrophotometer from the computer in order to calibrate, acquire and process the data.
3D printed box with a precision of 0.1 mm allows precise installation of the electronic and grating film.
Principle
Hardware
Software

## Slide 2
open-spectrophotometer
WHAT FOR ?
Simple design to understand how a spectrophotometer works, but precise enough to make real experiments.
Very cheap and accessible to everyone.
Determination of pigments concentration
Determination of pH using red cabbage
Chopped red cabbage was cooked in boiling water for 10 minutes to yield after filtration to a dark purple liquid.
The liquid was diluted by a factor 3 with water and either tartaric acid or sodium carbonate where added in various quantities to obtain a large color palette.
Red: acid, green: basic
Absorbance spectra of the 9 solutions
Linear regression
Slope: 46.12
Intercept: 0.03
R: 0.9973
R2: 0.9946
Blue patent V is the pigment that is present in Haribo smurfs sweets. Using a calibration curve with the pure pigment it is possible to determine the amount of colorant present in the sweets.
Calibration curve. In red the unknown.
Left: reference solutions. Right: Haribo
Florian, Océane and Luc Patiny, Michaël Zasso